RF transistor list
1 2 3 TO-92L	1 2 3 TO-202	1 2 3 TO-202N	1 2 3 TO-126	1 2 3 TO-220	1 2 3 TO-39	1 2 3 TO-60	T-31E

## Bipolar NPN Power Transistor
Transistor	Power	Gain	Voltage	Frequency	Mode	Case	Pin 123
2N3375	10W	5dB	28V	400MHz	FM/AM/SSB	TO-60
2N3553	2,5W	10dB	28V	175MHz	FM/AM	TO-39	C B E
2N3632	20W	7dB	28V	175MHz	FM	TO-60
2N3866	5W	10dB	28V	400MHz	WINTransceiver	TO-39	C B E
2N3924	4W	6dB	13,6V	175MHz	WINTransceiver	TO-39
2N4427	2W	10dB	12V	175MHz	WINTransceiver	TO-39
2N5108	1W	5dB	24V	1200MHz	WINTransceiver	TO-39
2N5109	3,5W	11dB	15V	200MHz	WINTransceiver	TO-39
2N5421	3W	9dB	13,5V	175MHz	WINTransceiver	TO-39
2N5913	2W	7dB	12,5V	175MHz	WINTransceiver	TO-39
2N5943	1W	8dB	15V	400MHz	FM	TO-39
2SC730	0,8W	10dB	13,5V	175MHz	FM	TO-39	C B E
2SC1096	10W			60MHz	FM	TO-220
2SC1173	10W			100MHz	FM/AM/SSB	TO-220
2SC1306	16W			30MHz	FM/AM/SSB	TO-220	B C E
2SC1307	16W	12dB	12V	30MHz	FM/AM/SSB	TO-220	B C E
2SC1590	5W	10dB	12,5V	136-174MHz	FM	TO-220	B E C
2SC1591	14W	7,5dB	12,5V	136-174MHz	FM	TO-220	B E C
2SC1678	5W			30MHz	WINTransceiver	TO-220	B C E
2SC1728	8W			80MHz	WINTransceiver	TO-202	E B C
2SC1729	14W	10dB	13,5V	175MHz	FM	T-31E
2SC1909	10W	14,5dB	13,5V	50MHz	FM/AM/SSB	TO-220	B C E
2SC1944	13W	11,1dB	12V	30MHz	WINTransceiver	TO-220	B C E
2SC1945	16W	14,5dB	12V	30MHz	FM/AM/SSB	TO-220	B E C
2SC1946	25W	6,7dB	13,5V	175MHz	FM	T-31E
2SC1946A	30W	10dB	13,5V	175MHz	FM	T-31E
2SC1947	3W	10dB	13,5V	175MHz	FM	TO-39	C B E
2SC1957	1,8W	17dB	12V	30MHz	WINTransceiver	TO-126	E C B
2SC1966	3W	7,8dB	13,5V	470MHz	FM	T-31E
2SC1967	7W	6,7dB	13,5V	470MHz	FM	T-31E
2SC1968	14W	3,7dB	13,5V	470MHz	FM	T-31E
2SC1968A	14W	5,4dB	13,5V	470MHz	FM	T-31E
2SC1969	18W	12dB	12V	30MHz	FM/AM/SSB	TO-220	B C E
2SC1970	1,5W	10dB	13,5V	175MHz	WINTransceiver	TO-220	B E C
2SC1971	7W	10dB	13,5V	175MHz	WINTransceiver	TO-220	B E C
2SC1972	14W	10dB	13,5V	175MHz	WINTransceiver	TO-220	B E C
2SC1973	1W			50MHz	WINTransceiver	TO-92L	B C E
2SC1974	13W	10dB	13,5V	30MHz	WINTransceiver	TO-220	B C E
2SC1975	4W	10dB	13,5V	30MHz	WINTransceiver	TO-220	B C E
2SC2028	1,8W			30MHz	WINTransceiver	TO-126	E C B
2SC2029	6W			30MHz	WINTransceiver	TO-220	B C E
2SC2036A	1,4W				WINTransceiver	TO-202	B C E
2SC2050	10W	12dB	13,5V	30MHz	FM/AM/SSB	TO-220	B C E
2SC2053	0,2W	15,7dB	12V	175MHz	FM/AM	TO-92L	B C E
2SC2055	0,25W	15,3dB	12V	175MHz	FM/AM	TO-92L	B C E
2SC2056	1,5W	9dB	12V	175MHz	FM	TO-39	C B E
2SC2075	4W		13,5V	27MHz	WINTransceiver	TO-220	B C E
2SC2078	4W	13dB	12V	100MHz	FM/AM	TO-220	B C E
2SC2086	0,45W	13dB	12V	175MHz	FM/AM	TO-92L	B C E
2SC2092	4W	13dB	12V	100MHz	FM/AM/SSB	TO-220	B C E
2SC2094	15W	8,8dB	13,5V	175MHz	FM/AM/SSB	T-31E
2SC2166	6W	13,8dB	12V	30MHz	FM/AM/SSB	TO-220	B C E
2SC2207	16W				WINTransceiver	TO-220	B C E
2SC2237	6W	13,8dB	13,5V	175MHz	FM	T-31E
2SC2312	18,5W			27MHz	FM/AM/SSB	TO-220	B C E
2SC2314	1,8W	17dB	12V	180MHz	FM/AM	TO-126	E C B
2SC2509	13W	14dB		30MHz	WINTransceiver	TO-220	B C E
2SC2527	60W				WINTransceiver	TO-220
2SC2538	0,6W	10dB	12V	175MHz	FM/AM	TO-92L	B C E
2SC2539	14W	14,5dB	13,5V	175MHz	FM	T-31E
2SC2660	30W			30MHz	WINTransceiver	TO-220
2SC2695	23W	1,9dB	13,5V	520MHz	FM	T-31E
2SC3001	6W	13dB	7,2V	175MHz	FM	T-31E
2SC3017	1W	11dB	13,5V	175MHz	FM	TO-39	C B E
2SC3018	3W	13dB	7,2V	175MHz	FM	T-31E
2SC3020	3W	10dB	12,5V	520MHz	FM	T-31E
2SC3021	7W	7,7dB	12,5V	520MHz	FM	T-31E
2SC3022	18W	4,8dB	12,5V	520MHz	FM	T-31E
2SC3103	2,8W	6,7dB	7,2V	520MHz	FM	T-31E
2SC3104	6W	4,8dB	7,2V	520MHz	FM	T-31E
2SC3133	13W	14dB	12V	1,5-30MHz	FM/AM/SSB	TO-220	B E C
2SC3297	15W			100MHz	WINTransceiver	TO-220
2SC3299	20W				WINTransceiver	TO-220
2SC3668	1W			100MHz	WINTransceiver
2SC3807	15W			260MHz	WINTransceiver	TO-126
2SC4137	4W			400MHz	WINTransceiver	TO-126
2SC4693					FM/AM	TO-92L	B C E
KTC1006	1W			100MHz	FM/AM	TO-92L	E C B
KTC1969	16W	12dB	12V	100MHz	FM/AM	TO-220	B C E
KTC2078	4W	11dB	12V	100MHz	FM/AM	TO-220	B C E
MRF161	5W	13,5dB	12,5V	225-500MHz	FM/AM	TO-220	B E C
MRF162	15W	13,5dB	12,5V	225-500MHz	FM/AM	TO-220	B E C
MRF163	25W	12dB	12,5V	225-500MHz	FM/AM	TO-220	B E C
MRF237	4W	12dB	18V	175MHz	WINTransceiver	TO-39
MRF260	5W	10dB	12,5V	136-174MHz	FM	TO-220	B E C
MRF261	10W	5,2dB	12,5V	136-174MHz	FM	TO-220	B E C
MRF262	14W	7,5dB	12,5V	136-174MHz	FM	TO-220	B E C
MRF264	30W	5,2dB	12,5V	136-174MHz	WINTransceiver	TO-220	B E C
MRF340	8W	13dB	28V	70MHz	WINTransceiver	TO-220	B E C
MRF342	24W	11dB	28V	70MHz	WINTransceiver	TO-220	B E C
MRF344	60W	6dB	28V	70MHz	WINTransceiver	TO-220
MRF454	80W	12dB	12,5V	1,5-30MHz	FM/AM/SSB
MRF455	60W	13dB	12,5V	1,5-30MHz	FM/AM/SSB
MRF475	12W	10dB	13,5V	1,5-30MHz	FM/AM/SSB	TO-220	B C E
MRF476	3W	15dB	13,5V	1,5-30MHz	FM/AM/SSB	TO-220	B C E
MRF477	40W	15dB	13,5V	1,5-30MHz	FM/AM/SSB	TO-220	B E C
MRF479	15W	10dB	13,5V	1,5-30MHz	FM/AM/SSB	TO-220
MRF485	15W	10dB	28V	1,5-30MHz	WINTransceiver	TO-220
MRF486	40W	15dB	28V	1,5-30MHz	WINTransceiver	TO-220
MRF496	40W	15dB	13,5V	1,5-30MHz	WINTransceiver	TO-220
MRF497	60W	10dB	13,5V	27-50MHz	WINTransceiver	TO-220	B E C
MRF517	0,75W	10dB	20V	1000MHz	WINTransceiver	TO-39
MRF607	1,75W	11,5dB	16V	175MHz	WINTransceiver	TO-39
MRF660	7W	5,4dB	12,5V	400-512MHz	WINTransceiver	TO-220
MS1226	30W	18dB	28V	30MHz	FM/AM/SSB
MS1227	20W	15dB	12,5V	30MHz	FM/AM/SSB

## FET Power Transistor
Transistor	Power	Gain	Voltage	Frequency	Mode	Case	Pin 123
MRF134	5W	14dB	28V	30-225MHz	FM/AM/SSB
MRF136	15W	16dB	28V	30-225MHz	FM/AM/SSB
MRF148A	30W	18dB	50V	2-225MHz	FM/AM/SSB
MRF171A	45W	19,5dB	28V	30-225MHz	FM/AM/SSB
MRF173	80W	13dB	28V	30-225MHz	FM/AM/SSB
MRF174	125W	11,8dB	28V	30-225MHz	FM/AM/SSB
MS1307	25W	dB	13,5V	30MHz	FM/AM/SSB	TO-220	G D S